## Slide 2
PRODUCT INTRODUCTION

## Slide 3
TRADITIONAL INSTALLATION
Channels with same Channel Number are lost
Poor isolation between adjacent channels
Signal quality issues
  Lots of interruptions
  Loss of 4dB (min) when combining antenna
PATENTED TECHNOLOGY

## Slide 4
Combining 2, 3 or 4 antenna for full HDTV reception has never been so easy
SMART AMP INSTALLATION
PATENTED TECHNOLOGY

## Slide 5
SMART AMP INSTALLATION
Better signal quality
More TV channels
Diplexing adjacent channels
Repositioning overlapping channels
POWER SUPPLY
PATENTED TECHNOLOGY

## Slide 6
How it works
HOW IT WORKS
Autoscan
360° OTA reception
DVB-T/T2 ATSC ISDB-T
4G/5G resillient
PATENTED TECHNOLOGY

## Slide 7
PRODUCT SPECIFICATIONS

## Slide 8
4 MODELS
7473L1
3 INPUTS
4G
7473L2
3 INPUTS
5G
7474L2
4 INPUTS
5G
PATENTED TECHNOLOGY
7474L1
4 INPUTS
4G

## Slide 9
PATENTED TECHNOLOGY
Scans all channels, amplifies the weak signals while keeping the strong channels
All output channels have an equal and stable output power
Treats even the most difficult situations with adjacent channels
Channels with the same frequency can be amplified in and re-located to the LTE band (switchable feature)
Fully automatic channel scan and process function upon start-up
FEATURES

## Slide 10
PATENTED TECHNOLOGY
Fully automatic recognition of the applied country channel plan
SAW filters for LTE (4G or 5G) rejection on all inputs
Outdoor weatherproof mast-head housing
DC Power over coax
All ports ESD protected
FEATURES

## Slide 11
SPECS LEAFLET
PATENTED TECHNOLOGY
SPECS
Parameter | Unit | KIT7473L1 | KIT7474L1 | KIT7473L2 | KIT7474L2
Inputs | - | 3 | 4 | 3 | 4
LTE rejection | - | 4G (>CH60) | 4G (>CH60) | 5G (>CH48) | 5G (>CH48)
Channel plan | - | VHF BIII + UHF Automatic channel plan selection |  |  | 
LTE band rejection | dB | >40 |  |  | 
Output | - | 1 |  |  | 
Output Power | dBµV | 85 |  |  | 
Frequency range | MHz | 174 - 862 |  |  | 
LTE band Re-use | - | L1 = CH61-69 (790MHz-862MHz) Switch ON-OFF |  | L2 = CH49-69 (694MHz-862MHz) Switch ON-OFF | 
Adjacent channel isolation | dB | >35 |  |  | 
Input sensitivity | dBµV | minimum 40 |  |  | 
Power | - | 12V/300mA (DC over coax) (350mA - 4 in) |  |  | 
Power Supply | - | External power supply (ref. 2437 - 2 out) |  |  | 
Dimensions | mm | 120 x 115 x 50 |  |  | 
Operating temperature | °C | -20 to +50 |  |  | 

## Slide 12
PRODUCT INSTALLATION

## Slide 13
ANTENNA 1
Smart Amp
Power
Supply
TV1
TV2
DC
How it works
1 ANTENNA
PATENTED TECHNOLOGY

## Slide 14
ANTENNA 1
Smart Amp
Power
Supply
TV1
TV2
DC
LTE1
CH21-60
REF. 7473L1
LTE1
LTE1
CH21-60
LTE1 = LTE800 = 4G
Everything above 790MHz is filtered out
PATENTED TECHNOLOGY

## Slide 15
ANTENNA 1
Smart Amp
Power
Supply
TV1
TV2
DC
LTE2
CH21-48
REF. 7473L2
LTE2
LTE2
CH21-48
LTE2 = LTE700 = 5G
Everything above 694MHz is filtered out
PATENTED TECHNOLOGY

## Slide 16
ANTENNA 1
Smart Amp
DC
ANTENNA 3
ANTENNA 2
3 ANTENNA
PATENTED TECHNOLOGY

## Slide 17
ANTENNA 1
Smart Amp
DC
ANTENNA 3
ANTENNA 2
CH21-48/60
LTE2/1
3 ANTENNA
PATENTED TECHNOLOGY

## Slide 18
ANTENNA 1
Smart Amp
DC
ANTENNA 3
ANTENNA 2
CH21-48/60
LTE2/1
Duplicate channel feature ON
CONVERSION ON
PATENTED TECHNOLOGY

## Slide 19
ANTENNA 1
Smart Amp
DC
ANTENNA 3
ANTENNA 2
CH21-48/60
LTE2/1
CONVERSION ON
DUPLICATED CHANNELS IN LTE BAND
4G: 62 – 64 – 66 - … in steps of 2, then 61 – 63 –…
5G: 50 – 52 – 54 - … in steps of 2, then 49 – 51 – …
PATENTED TECHNOLOGY

## Slide 20
ANTENNA 1
Smart Amp
DC
ANTENNA 3
ANTENNA 2
CH21-48/60
LTE2/1
CH30
CH30
CH30
conv.
CH30
CONVERSION ON
Duplicated channels ON:
weakest channel is converted to LTE band ;
CH30 > CH30  CH30 is transmitted
 CH30 is converted to LTE band
PATENTED TECHNOLOGY

## Slide 21
ANTENNA 1
Smart Amp
DC
ANTENNA 3
ANTENNA 2
CH21-48/60
LTE2/1
CH30
CH30
CH30
CH40
CH40
CH40
CH40
conv.
CH30
conv.
CONVERSION ON
Duplicated channels ON:
weakest channel is converted to LTE band ;
CH30 > CH30  CH30 is transmitted
 CH30 is converted to LTE band
CH40 < CH40  CH40 is converted to LTE band
 CH40 is transmitted
PATENTED TECHNOLOGY

## Slide 22
ANTENNA 1
Smart Amp
DC
ANTENNA 3
ANTENNA 2
CH21-48/60
LTE2/1
Duplicate channel feature OFF
CONVERSION OFF
PATENTED TECHNOLOGY

## Slide 23
ANTENNA 1
Smart Amp
DC
ANTENNA 3
ANTENNA 2
CH21-48/60
LTE2/1
CH30
CH30
CH30
CH40
CH40
CH40
Duplicated channels OFF:
weakest channel is rejected;
CH30 > CH30  CH30 is transmitted
 CH30 is rejected
CH40 < CH40  CH40 is rejected
 CH40 is transmitted
CONVERSION OFF
PATENTED TECHNOLOGY

## Slide 24
AUTOSCAN
PATENTED TECHNOLOGY
FORCE CHANNEL SCAN
= RESET = REPROGRAM
Unpower
Repower within 6 sec
Status LED will blink when scanning
If power interruption (>6 sec)
= no reprogram = settings are kept
PLUG-AND-PLAY
Plug in Power Supply
Status LED will blink when scanning
Status LED solid when autoscan ready
This can take up to 20 seconds

## Slide 25
CONCLUSIONS

## Slide 26
PATENTED TECHNOLOGY

## Slide 27
Masz pytanie?
Napisz do nas!
sklep@dmtrade.pl
PATENTED TECHNOLOGY